ISO XXXX1:2019(E)

ISO/TC 211/WG 9

Secretariat: SIS

Geographic information — Geodetic register installation guide

Information géographique — Guide d’installation du registre géodésique

© ISO 2019, Published in Switzerland.

All rights reserved. Unless otherwise specified, no part of this publication may be reproduced or utilized otherwise in any form or by any means, electronic or mechanical, including photocopying, or posting on the internet or an intranet, without prior written permission. Permission can be requested from either ISO at the address below or ISO’s member body in the country of the requester.

ISO copyright office

Ch. de Blandonnet 8 • CP 401

CH-1214 Vernier, Geneva, Switzerland

Tel.  + 41 22 749 01 11

Fax  + 41 22 749 09 47

copyright@iso.org

www.iso.org

Contents

TOC \o "1-2" \h \z \u   Foreword .     PAGEREF _Toc587283140 \h  1

0 Introduction .     PAGEREF _Toc16529006 \h  1

1 Scope .     PAGEREF _Toc650831454 \h  1

2 Normative references .     PAGEREF _Toc126242700 \h  1

3 Terms, definitions, symbols and abbreviated terms .     PAGEREF _Toc657734170 \h  1

3.1 Symbols .     PAGEREF _Toc454359538 \h  1

4 Prerequisites .     PAGEREF _Toc450506382 \h  1

4.1 Hardware requirements .     PAGEREF _Toc492968170 \h  1

4.2 System requirements .     PAGEREF _Toc232158322 \h  1

4.3 Skill requirements .     PAGEREF _Toc231468793 \h  1

5 Installation .     PAGEREF _Toc900827488 \h  1

5.1 Prerequisites .     PAGEREF _Toc807046833 \h  1

5.2 Steps .     PAGEREF _Toc497059246 \h  1

5.3 Database connection (hibernate.connection.xml) .     PAGEREF _Toc21964500 \h  1

5.4 Database parameters (hibernate.properties.xml) .     PAGEREF _Toc522441436 \h  1

5.5 Registry configuration (registry.configuration.xml) .     PAGEREF _Toc328488631 \h  1

5.6 Registry client configuration (client.configuration.xml) .     PAGEREF _Toc392300312 \h  1

Annex A (informative) Default users .     PAGEREF _Toc833502691 \h  1

Bibliography .     PAGEREF _Toc965016146 \h  1

# Foreword

ISO (the International Organization for Standardization) is a worldwide federation of national standards bodies (ISO member bodies). The work of preparing International Standards is normally carried out through ISO technical committees. Each member body interested in a subject for which a technical committee has been established has the right to be represented on that committee. International organizations, governmental and non-governmental, in liaison with ISO, also take part in the work. ISO collaborates closely with the International Electrotechnical Commission (IEC) on all matters of electrotechnical standardization.

Attention is drawn to the possibility that some of the elements of this document may be the subject of patent rights. ISO shall not be held responsible for identifying any or all such patent rights. Details of any patent rights identified during the development of the document will be in the Introduction and/or on the ISO list of patent declarations received (see www.iso.org/patents).

Any trade name used in this document is information given for the convenience of users and does not constitute an endorsement.

This document was prepared by Technical Committee ISO/TC 211, Geographic information.

This document is amongst a series of International Standards dealing with the conversion of systems of writing produced by Technical Committee ISO/TC 211, Geographic information, WG 9 Information management.

This is the second edition of this document.

Copyright © 2014-2018 Statens kartverk. 2019 ISO/TC 211.

# 0  Introduction

0.1 General

This document describes installation requirements and procedures for the ISO Geodetic Registry.

The intended audiences are operators and developers of the ISO Geodetic Registry system.

0.2 The ISO Geodetic Registry

The ISO Geodetic Registry is a structured database of coordinate reference systems and transformations that is accessible through an on-line registry system.

This Registry is provided under the auspices of ISO Technical Committee 211 on geographic information/geomatics and conforms to ISO standards:

ISO 19111:2007;

ISO 19127;

ISO 19135:2005, ISO 19135-1 and ISO 19135-2:2012.

Geographic information — Geodetic register installation guide

# 1  Scope

This document describes installation requirements and procedures for the ISO Geodetic Registry.

# 2  Normative references

The following documents are referred to in the text in such a way that some or all of their content constitutes requirements of this document. For dated references, only the edition cited applies. For undated references, the latest edition of the referenced document (including any amendments) applies.

ISO 19127,  Geographic information — Geodetic register

# 3  Terms, definitions, symbols and abbreviated terms

For the purposes of this document, the terms and definitions given in ISO 19127 apply.

ISO and IEC maintain terminological databases for use in standardization at the following addresses:

ISO Online browsing platform: available at http://www.iso.org/obp

IEC Electropedia: available at http://www.electropedia.org

## 3.1 Symbols

### 3.1.1 <Tomcat7>

path to Apache Tomcat 7

EXAMPLE   /var/lib/tomcat7

### 3.1.2 <dbserver>

host name or IP address of the PostgreSQL server

### 3.1.3 <dbport>

port of the PostgreSQL server

### 3.1.4 <dbname>

name of the PostgreSQL database

### 3.1.5 <dbuser>

PostgreSQL login role that has full rights on the <dbname> database

### 3.1.6 <dbpassword>

password of <dbuser>

### 3.1.7 <host>

host name or IP address of the installation server

### 3.1.8 <port>

port where Apache Tomcat listens for HTTP requests

EXAMPLE  8080

# 4  Prerequisites

## 4.1 Hardware requirements

Server load is difficult to predict, therefore live testing remains the best way to determine what hardware the ISO Registry instance will require in production. The values given below refer to the minimum available hardware to run the ISO Registry instance with five concurrent users.

2 GHz+ CPU

2048 MB RAM

10 GB database space

## 4.2 System requirements

Table 1

| Java version | Oracle JRE / JDK ; 1.7 ; . OpenJDK (IcedTea) ; 2.4 ; . |
| --- | --- |
| Operating systems for server | Microsoft Windows Linux (Ubuntu LTS 14.04+) |
| Application server | Apache Tomcat ; 7.0.x ; . |
| Database | PostgreSQL ; 9.1, 9.2, 9.3 ; . |
| Web browsers – desktop | Microsoft Internet Explorer (Windows) ; 10, 11 ; . Mozilla Firefox (all platforms) ; latest stable version ; . Google Chrome (Windows and Mac) ; latest stable version ; . |
| Web browsers – mobile | Android (Android) ; the default Android browser ; . Chrome (Android and iOS) ; latest stable version ; . |

## 4.3 Skill requirements

This document assumes that you:

are familiar with administrating Linux systems

have root access to the server used for installation

# 5  Installation

## 5.1 Prerequisites

The steps in this section depend on the following assumptions.

The following components have been installed on the server:

OpenJDK 7 or Oracle JDK/JRE 7

Apache Tomcat 7.0.x

The server can connect to a PostgreSQL instance and:

the database <dbname> for the ISO Registry was created

the database user <dbuser> with password <dbpassword> exists and has full rights on the <dbname> database

The server can connect to an SMTP server that will deliver mails sent by the registry software.

The commands shown work on servers running Ubuntu LTS 14.04 (and possibly later Ubuntu versions). In case your server runs a different distribution you must modify the commands to fit that platform.

## 5.2 Steps

Load the database dump iso-gcp-minimal.backup into the isoreg database (for example, through PgAdmin).

The dump contains a minimal version of the ISO Registry of Geodetic Codes and Parameters, including example users. For further details, see configuration.

Copy the web archive iso-registry-client.war to <Tomcat7>/webapps, the directory that contains Tomcat’s webapps (e.g. /var/lib/tomcat7/webapps).

Apache Tomcat should unpack the web archive to the sub-directory iso-registry-client.

Stop Apache Tomcat

service tomcat7 stop

Change to the directory iso-registry-client/WEB-INF/classes and edit the following configuration files:

registry.configuration.xml

client.configuration.xml

hibernate.connection.xml and

hibernate.properties.xml.

For a list of all configuration settings, see section 1.6.

Start Apache Tomcat +

service tomcat7 start

To access the ISO Registry of Geodetic Codes and Parameters, open a browser and navigate to http:// server URL>/iso-registry-client. For example, with Tomcat running on port 8080 on localhost, the URL would be http://localhost:8080/iso-registry-client. == Configuration

## 5.3 Database connection (hibernate.connection.xml)

| hibernate.connection.username | <dbuser> |
| --- | --- |
| hibernate.connection.password | <dbpassword> |
| hibernate.connection.url | jdbc:postgresql://<dbhost>:<dbport>/isoreg |

## 5.4 Database parameters (hibernate.properties.xml)

| hibernate.hbm2ddl.auto | validate – for standard production use update – when performing a software update create – when installing for the time |
| --- | --- |

## 5.5 Registry configuration (registry.configuration.xml)

| mail.enabled | true – mail sending is enabled false – mail sending is disabled |
| --- | --- |
| mail.from.name | Mail name used in From header |
| mail.from.address | E-mail address used in From header |
| mail.smtp.auth | Switch to activate SMTP authentication (true, false) |
| mail.smtp.starttls.enable | Switch to activate STARTTLS SMTP authentication (true, false) |
| mail.smtp.host | Host name or IP address of SMTP server |
| mail.smtp.port | Port number of SMTP server (TLS: 587, plain: 25) |
| mail.smtp.user | User name used for SMTP authentication |
| mail.smtp.password | Password used for SMTP authentication (plain text) |

## 5.6 Registry client configuration (client.configuration.xml)

| basePath | If you run Apache Tomcat behind a reverse proxy this parameters must be set to the context path used by external clients, preceded by a tilde. If e.g. the registry is accessed from the outside via the URL http://registry.isotc211.org/gcp the parameter must be set to ~/gcp. In environments without a reverse proxy this parameters must be left empty. |
| --- | --- |

Annex A

(informative)

# Default users

The minimal database in iso-gcp-minimal.backup contains the following users:

Table A.1

| Login (e-mail) | Password | Roles |
| --- | --- | --- |
| admin@example.org | a | Administrator |
| controlbody@example.org | c | Control Body |
| regman@example.org | r | Register Manager |
| owner@example.org | o | Register Owner |
| submitter@example.org | s | Submitter |
| poc@example.org | p | Point of Contact of “Example Organization” |

# Bibliography

[1]  ISO 19111:2007,  Geographic information — Spatial referencing by coordinates

[2]  ISO 19135:2005,  Geographic information — Procedures for item registration

[3]  ISO 19135-1,  Geographic information — Procedures for item registration — Part 1: Fundamentals

[4]  ISO 19135-2:2012,  Procedures for item registration — Part 2: XML schema implementation